## Slide 1: Optimal Moving Average Estimation of Noisy Random Walks using Allan Variance-informed Window Length
Hossein Haeri1, Behrad Soleimani2, and Kshitij Jerath1
1 Department of Mechanical Engineering, University of Massachusetts Lowell
2 Department of Electrical and Computer Engineering, University of Maryland
American Control Conference (ACC2022)
June 8, 2022 | Atlanta, GA

## Slide 2: Is Your Data Still Relevant?
[1] Data represents customer rating of a particular product on Amazon (https://nijianmo.github.io/amazon/index.html)
5
4
3
2
1
Time
Data1
Current time plane
Notes: Let’s consider the user ratings of a certain product on Amazon
We want to estimate the current quality of the product, but we know not all the ratings have the same value.
In fact, the product used to receive good ratings initially, but after some time it got some bad ratings indicating that the quality of the product might have gone bad.
The question is if we want to build a model for predicting the current quality of the product, what portion of the data should be used to train that model with?

## Slide 3: Is Your Data Still Relevant?
[1] Data represents customer rating of a particular product on Amazon (https://nijianmo.github.io/amazon/index.html)
Time
5
4
3
2
1
Data1
Current time plane
Notes: You can use some windowing techniques to degrade the values of the old measurements but again the question is how wide that window should be?

## Slide 4: Moving Average Estimation: What is a Good Window Length?
Despite the vast investigation in advanced data filtering techniques, Simple Moving Average Estimations (SMAE) are still among the widely used filtering solutions in many fields of research.
The challenge of systematically selecting an appropriate timescale or window length over which to average measurements persists to this day.
This is mainly because in many scenarios the signal and noise characteristics are not available in prior or have an unforeseen dynamics.

## Slide 5: Estimation of Noisy Random Walks
The goal is to estimate the value of a time-varying parameter , based on historical measurements .
Dynamics of the target parameter may be modeled as a random walk stochastic with a white Gaussian process noise , i.e.,
Measurements of the time-varying parameter are themselves assumed to be corrupted by Gaussian white noise, i.e.,

## Slide 6: Optimal Simple Moving Average Estimation of Noisy Random Walks
Simple Moving Average Estimation (SMAE) attempts to recover the value of the parameter at the last timestep, , given historical measurements .
The optimal window length is referred to as the characteristic timescale, which is the window length (or timescale) that minimizes the mean-square estimation error, i.e.,

## Slide 7: O-SMAE of Noisy Random Walks
Theorem 1: If the drift signal is realized from a random walk process and the measurements are corrupted with white Gaussian noise, then the characteristic timescale is given by:
where denotes rounding to the adjacent integer with the smaller estimation error.

## Slide 8: Allan Variance as a Measure of Signal Bias Variation at a Particular Timescale
The non-overlapping Allan Variance, also known as two-sample variance, for a time series is defined as a function of timescale as:
where is the average of measurements in the window of size calculated at the time step :

## Slide 9: Allan Variance as a Measure of Signal Bias Variation at a Particular Timescale
The non-overlapping Allan Variance, also known as two-sample variance, for a time series is defined as a function of timescale as:
where is the average of measurements in the window of size calculated at the time step :

## Slide 10: Estimating Allan Variance
Allan Variance can be naively estimated as:
AVAR can be also calculated in as1:
where is the accumulated signal value at
the time step .
[1] Elfeki, Amro, and Jarbou Bahrawi. "Application of the random walk theory for simulation of flood hazards: Jeddah flood 25 November 2009." International journal of emergency management 13.2 (2017): 169-182.

## Slide 11: Allan Variance of Noisy Random Walks Yields Characteristic Timescale
Theorem 2: If the drift signal is realized from a random walk process and the measurements are corrupted with white Gaussian noise, then timescale minimizing Allan Variance is an unbiased estimate of the characteristic timescale , i.e.,

## Slide 12: Example of Optimal Simple Moving Average Estimation (O-SMAE) using AVAR

## Slide 13: Allan Variance of Noisy Random Walks Yields Characteristic Timescale
Comparing
  numerically estimated AVAR using only the measurement signal, vs.
  analytically derived AVAR assuming is known,
confirms the accuracy of the AVAR estimation.
Numerical AVAR values have been averaged over 100 Monte Carlo simulations.
While there may be a small error in the size of the optimal window length determined via AVAR, the error as the number of available measurements increases.

## Slide 14: AVAR-Suggested Window Length for Other Signal Types
We have also showed that AVAR-suggested window length yields near-optimal results with non-random walk signals1.
[1] Haeri, Hossein, Craig E. Beal, and Kshitij Jerath. "Near-optimal moving average estimation at characteristic timescales: An Allan Variance approach." IEEE Control Systems Letters 5.5 (2020): 1531-1536.

## Slide 15: Conclusion and Future Work
We can optimally perform moving average estimation of noisy random walks by systematically selecting an Allan variance-informed window length, without the need to rely on heuristics or any prior knowledge of signal and noise characteristics.
In future, we intend to use Dynamic Allan Variance1 to adaptively estimate the characteristic timescale on-the-fly.
[1] Galleani, Lorenzo, and Patrizia Tavella. "The dynamic Allan variance IV: Characterization of atomic clock anomalies." IEEE Transactions on Ultrasonics, Ferroelectrics, and Frequency Control 62.5 (2015): 791-801.

## Slide 16
Optimal Moving Average Estimation of Noisy Random Walks using Allan Variance-informed Window Length Hossein Haeri, Behrad Soleimani, and Kshitij Jerath
American Control Conference (ACC2022) | June 8, 2022 | Atlanta, GA

## Slide 17: Motivation
Despite the vast investigation in advanced data filtering techniques, Simple Moving Average Estimations (SMAE) are still among the widely used filtering solutions in many fields of research such as:
trend forecasting1 communication systems2, econometrics3, circuit design4, cardiac signal analysis5 and, general data monitoring6.
The challenge of systematically selecting an appropriate timescale or window length over which to average measurements persists to this day.
[1] shynkevich, 2014 [2] luo, 2012 [3] Ellis, 2005 [4] forbes, 2013 [5] chen, 2003 [6] chen, 2017